## Slide 1: On Developing and Optimizing New Machine Learning Techniques to Analyze Mobility Parameters and Gait Patterns for Healthcare Purposes
Presenter: Donovan Orn

## Slide 2: Overall Goal
How can we use mobility parameters collected from wearable sensors to assess health?

## Slide 3: Motivation wearable Sensors and health
Widespread use of wearable devices.
Can we utilize the data collected from these devices to remotely predict potential health hazards?
Need for a systematic way to use movement patterns to access health.

## Slide 4: Machine Learning
What
Takes in data
Uses pattern analysis
Predicts result
Why
Real time predictions
Can catch the disease early
Can be used to alert Dr. and patient

## Slide 5: Project Goal
Improve machine learning models by developing a methodology for finding the best data reduction techniques.

## Slide 6: Introducing the data
UPDRS and H&Y are from early stages of Parkinson’s disease.
Shimmer R3
(inertial measurement Unit (IMU))
37 Features
Groups | Control | Geriatrics
Number of Subjects | 10 | 10
Gender(M/F) | 5:5 | 4:6
Age | 64 ± 8.4 | 81 ± 4.1
UPDRS III |  | 
H & Y |  | 
PD
10
5:5
63.8 ± 9.3
12.7 ± 6.0
1.7 ± .09

## Slide 7: Significance of Data Reduction
Too Many Features
Overfitting
  High training accuracy
  Less accurate when predicting new individuals
Data Reduction
Removes irrelevant and redundant data.
Data Reduction Categories:
  Filter Based – MIGMC and MSNR&MC
  Wrapper Based – Genetic Algorithm
  Dimensionality Reduction – PCA
  Embedded methods
Dummy Training Individuals
Dummy New Individuals
Key
Over-fit model
Fit model

## Slide 8: Assessment of Data Reduction Techniques
Number of features selected
Classification accuracy
  10 random 10-fold cross-validations
  Median and standard deviation
Completion time
Compared (PD and HE), (PD and GE), (GE and HE)

## Slide 9: Filter based Methods
Maximum Signal to noise ratio Minimum Correlation (MSNR&MC2)
Maximum Information Gain Minimum Correlation (MIGMC)

## Slide 10: Variations of MIGMC and MSNR&MC
Both MIGMC and MSNR&MC are filter based methods.
MIGMC has a threshold to stop while MSNR&MC2 does not
To have a fair comparison between these two methods:
  Variation of MSNR&MC2 with threshold was implemented (MSNR&MC)
  Variation of MIGMC without threshold was implemented (MIGMC2)

## Slide 11: Genetic Algorithm (GA)

## Slide 12: Principal component Analysis (pca)
Parkinson’s and healthy elderly, three principal components compared to two principle components.
Dimensionality reduction method
  Components are created from the original feature set by projecting them onto lower dimensions called principal components
  3 Components are used
  Tested Highest Explained Variance (HEV) component, First 2 HEV, and All components

## Slide 13: Results: # Features Selected
Feature Selection | # Features PD and HE | # Features PD and GE | # Features in GE and HE
GA | 6 | 4 | 1
MIGMC | 1 | 4 | 1
MIGMC2 | 3.6 ± 2.3 | 5.3 ± 3.4 | 2.3 ± 1.8
MSNR&MC | 10 | 9 | 12
MSNR&MC2 | 6.5 ± 5.1 | 6.8 ± 5.8 | 6.4 ± 3.8
PCA | 1 | 2 | 1
# Features Selected

## Slide 14: Results: performance
Classification Accuracy
Computation Time
Feature Selection | Average Comp. Time
GA | 8423.5425 or 2h 20m 23.5425s
MIGMC | 0.214s
MIGMC2 | 0.3047s
MSNR&MC | 0.3527s
MSNR&MC2 | 0.3579s
PCA | 0.0078s

## Slide 15: Conclusions
Results show that AdaBoost is the most robust machine learning classifier
GA followed by MSNR&MC2 and MIGMC2 showed the highest performance
Computation Time of GA was vastly higher than other feature selection techniques
GA performs the best when computational resources are available
MSNR&MC2 and MIGMC2 are the best when there are limited computational resources

## Slide 16: Next Steps
Improve the genetic algorithm feature selection.
  Correlation based mutation function
  Correlation based crossover function
Goal to improve performance
  Accuracy – improving search space
  Completion time – reducing search space

## Slide 17: Questions and answers

## Slide 18: Maximum Signal to noise ratio Minimum Correlation (MSNR&MC2)
Signal to Noise Ratio Rank
MSNR&MC algorithm
SNR Rank
Feature with highest SNR Score
Feature With Lowest SNR Score
Find Highest Correlated Pair
Remove Lowest in rank

## Slide 19: Maximum Information Gain Minimum Correlation (migmc)

## Slide 20: Fitness/Optimization Function
If #of Features = 0
Individual Fitness = 0
For individual in generation
Features = all positions, True
Scale features
Build Models
False
True